I2C BUS ROUTINES
(Modified for SC126)

This document covers the use of the software I2C bus routines and the hardware connections to the I2C connector
on the Steve Cousins SC126 Z180 single board computer and some assembler code examples.
The design supports single master mode only while many devices can be connected to the bus.
No support for clock stretching is provided.

The following routines are used to control the I2C bus.

1000 - PORT_INIT:	Configures the 8 bit control register IC – U6.
1017 - I2C_RESET:	Reset the I2C bus ready for communication.
1025 – I2C_START:	Send a start bit.
1032 – I2C_STOP:	Send a stop bit.
1045 – I2C_TX:	Transmit a single byte to the bus, read the ACK bit.
1052 – I2C_RX:	Receive a single byte from the bus, Send a NACK bit.
1155 - ACK_POLLING:	Wait for the device to send an acknowledge bit then issue a stop bit.
10DE – I2C_WR:	Sequence to send a byte to a specified devices memory address.
1111 – I2C_RD	:	Sequence to read a byte from a specified devices memory address.
116F – I2C_BLOCK_WR:	Transfer a block of data from memory to EEPROM.
11CF – I2C_BLOCK_RD:	Transfer a block of data from EEPROM to memory.
117A -	ALT_BLOCK_WR:	Set EEPROM address then transfer block of data from memory to EEPROM.
11DA – ALT_BLOCK_RD:	Set EEPROM address then transfer block of data from EEPROM to memory.
11F8 - I2C_RX2:	Receive a byte of data from the device.
120B - SEND_ACK:	Send an ACK bit.
1215 - SEND_NACK:	Send a NACK bit.
121C – RESTART:	Perform a restart to continue using the bus.
1226 – RTC_BLOCK_WR:	Sequence to send 8 bytes from a config table to	the DS1307 RTC.
124D – RTC_BLOCK_RD:	Sequence to receive 8 bytes from the DS1307 RTC to a config table.

Connections to the I2C port on the SC126 computer.	SC138 I2C Memory Card

ERROR CONDITIONS

The I2C_BLOCK_WR and I2C_BLOCK_RD routines will exit with an error code shown below if an error should occur. The error code will be saved to address 1B03.

Block write errors:	Code

No 'ACK' on EEPROM device address	01.
No 'ACK' on memory address high byte	02.
No 'ACK' on memory address low byte	03.
No 'ACK' on data byte	04.

Byte sent to EEPROM not the same as byte read back	FF.
The byte written to EEPROM is read back and compared with the same byte in the computers memory before moving on to the next. An error will exit the routine.

Block read errors:	Code

No 'ACK' on EEPROM device address	11.
No 'ACK' on memory address high byte	12.
No 'ACK' on memory address low byte	13.
No 'ACK' on EEPROM device address before reading data	14.

Applies to both:

The memory address where the error occurred will be saved in RAM locations 1B04 – 1B05.
The software will exit on the first error and show -Err on the LED display.

End address lower than start address	80.
The software will immediately exit and show -Err on the display.

No error	00.

These routines only indicate an error by showing -Err on the display.

I2C_RX2
RTC_BLOCK_WR
RTC_BLOCK_RD

EXAMPLE CODE

Writing one byte to a 24LC08 EEPROM. Load register A with data byte before calling this routine.

2000	F5	PUSH	AF	Push the data byte on the stack.
2001	CD	00	10	CALL	PIO_INIT	;Initialise the PIO and reset the bus.
2004	3E	A0	LD	A, A0
2006	32	02	1B	LD	(1B02), A	;Save EEPROM device address.
2009	CD	25	10	CALL	I2C_START	;Send a start bit.
200C	3A	02	1B	LD	A, (1B02)	;Get saved EEPROM device address.
200F	CB	87	RES	0, A	;Indicate a write to EEPROM.
2011	CD	45	10	CALL	I2C_TX	;Transmit the EEPROM address.
2014	D2	53	03	JP	NC, ERROR_MSG	;Indicate ACK error if any.
2017	3E	00	LD	A, 00
2019	CD	45	10	CALL	I2C_TX	;Select EEPROM memory address 00h.
201C	D2	53	03	JP	NC, ERROR_MSG	;indicate ACK error if any.
201F	F1	POP	AF	;Pop the data byte off the stack.
2020	CD	45	10	CALL	I2C_TX	;Transmit a data byte to EEPROM.
2023	D2	53	03	JP	NC, ERROR_MSG	;Indicate ACK error if any.
2026	CD	32	10	CALL	I2C_STOP	;Send a stop bit.
2029	CD	55	11	CALL	ACK_POLLING	;Wait for EEPROM to	;acknowledge the transfer	;before continuing.
202C	C9	RET

Reading one byte from a 24LC08 EEPROM. On return the data byte read from the EEPROM is in register A.

202D	CD	00	10	CALL	PIO_INIT	;Initialise the PIO and reset the bus.
2030	3E	A0	LD	A, A0	;Device address.
2032	32	02	1B	LD	(1B02), A	;Save EEPROM device address.
2035	CD	25	10	CALL	I2C_START	;Send a start bit.
2038	3A	02	1B	LD	A, (1B02)	;Get saved EEPROM device address.
203B	CB	87	RES	0, A	;Indicate a write to EEPROM.
203D	CD	45	10	CALL	I2C_TX	;Transmit the EEPROM address.
2040	D2	53	03	JP	NC, ERROR_MSG	;Indicate an error if any.
2043	3E	00	LD	A, 00
2045	CD	45	10	CALL	I2C_TX	;Select EEPROM memory address 00h.
2048	D2	53	03	JP	NC, ERROR_MSG	;indicate an error if any.
204B	CD	1C	12	CALL	RESTART	;Send restart bit.
204E	3A	02	1B	LD	A, (1BO2)	;Get EEPROM device address.
2051	CB	C7	SET	0, A	;Indicate a read from EEPROM.
2053	CD	45	10	CALL	I2C_TX	;Transmit the EEPROM address.
2056	D2	53	03	JP	NC, ERROR_MSG	;Indicate an error if any.
2059	CD	F8	11	CALL	I2C_RX2	;Read the data byte from EEPROM.
205C	CD	15	12	SEND_NACK	;Indicate no more bytes to receive.	205F	CD	32	10	CALL	I2C_STOP	;Send a stop bit.
2062	C9	RET

A block write using a 24LC512 EEPROM. Sending 256 bytes.

2000	21	00	80	LD	HL, 8000	;Block start address.
2003	11	FF	80	LD	DE, 80FF	;Block end address.
2006	CD	6F	11	CALL	I2C_BLOCK_WR	;Do a block write.
2009	76	HALT

A block read example using a 24LC512 EEPROM. Receiving 256 bytes.

200A	21	00	80	LD	HL, 8000	;Block start address.
200D	11	FF	80	LD	DE, 80FF	;Block end address.
2010	CD	CF	11	CALL	I2C_BLOCK_RD	Do a block read.
2013	76	HALT

An alternative block write using a 24LC512 EEPROM that allows changing of slave address.

2000	CD	00	10	CALL	PIO_INIT	;Initialise the PIO and reset the bus.
2003	3E	A1	LD	A, AE	;Set EEPROM device address.
2005	21	00	80	LD	HL, 8000	;Block start address.
2008	11	FF	80	LD	DE, 80FF	;Block end address.

200B	CD	7A	11	CALL	117A	;Write block to EEPROM.
200E	76	HALT

An alternative block read using a 24LC512 EEPROM that allows changing of slave address.

2000	CD	00	10	CALL	PIO_INIT	;Initialise the PIO and reset the bus.
2003	3E	A1	LD	A, AF	;Set EEPROM device address.
2005	21	00	80	LD	HL, 8000	;Block start address.
2008	11	FF	80	LD	DE, 80FF	;Block end address.

200B	CD	DA	11	CALL	11DA	;Read block from EEPROM.
200E	76	HALT

Writing a config table to the DS1307 RTC

3000	21	00	19	LD	HL, 1900	;Start address of config table.
3003	CD	26	12	CALL	RTC_BLOCK_WR
3006	76	HALT

Reading the DS1307 RTC and saving to a config table.

3007	21	00	19	LD	HL, 1900	;Start address of config table.
300A	CD	4D	12	CALL	RTC_BLOCK_WR
300D	76	HALT

CONFIG_TABLE:

1900	0x00
1901	0x00
1902	0x00
1903	0x00
1904	0x00
1905	0x00
1906	0x00
1907	0x13

ASSEMBLER LISTING OF I2C BUS ROUTINES

PORT_B_DATA	NOT USED	;PIO data register.
PORT_B_CNTRL	0x0C	;Control register.
PIO_B_MODE	NOT USED	;Current PIO mode.
PIO_B_IO_CONF	0x1B01	;Current configuration of i2c control register.
EEPROM_ADDR	0x1B02	; Address of EEPROM.
SCL	bit 0	;Serial clock.
SDA_WR	bit 7	;Serial data write.
SDA_RD	bit 7	Serial data read.

; The contents of these variables are invalid unless “-ERR” is displayed.
ERROR_CODE	0x1B03	; Error type.
HI_ADDR	0x1B04	; High byte of address that error occurred.
LO_ADDR	0x1B05	; Low byte of address that error occurred.

ORG:	0x1000

PORT_INIT:
1000	3E	FF	LD	A, FF
1002	32	00	1B	LD	(PIO_B_MODE), A
1005	00	NOP
1006	00	NOP
1007	3E	8D	LD	A, 8D	;Set up i2c control register.
1009	32	01	1B	LD	(PIO_B_IO_CONF), A
100C	D3	0C	OUT	(PORT_B_CNTRL), A
100E	00	NOP
100F	00	NOP
1010	00	NOP
1011	00	NOP
1012	3E	00	LD	A, 00
1014	32	03	1B	LD	(ERROR_CODE), A	;Clear error indication.
I2C_RESET:
1017	06	0A	LD	B, 0A	;Do the following 10 times.
LOOP1:
1019	CD	68	10	CALL	SCL_CYCLE
101C	10	FB	DJ	NZ, LOOP1	;Cycle SCL 10 times while SDA
;is high.
101E	CD	9B	10	CALL	SCL_IN
1021	00	NOP
1022	00	NOP
1023	00	NOP
1024	C9	RET

I2C_START:
1025	CD	8B	10	CALL	SDA_OUT	;SDA = L
1028	CD	66	11	CALL	DELAY
102B	CD	AB	10	CALL	SCL_OUT	;SCL = L
102E	CD	66	11	CALL	DELAY
1031	C9	RET

I2C_STOP:
1032	CD	8B	10	CALL	SDA_OUT	;SDA = L
1035	CD	66	11	CALL	DELAY
1038	CD	9B	10	CALL	SCL_IN	;SCL = H
103B	CD	66	11	CALL	DELAY
103E	CD	7B	10	CALL	SDA_IN	SDA = H
1041	CD	66	11	CALL	DELAY
1044	C9

I2C_TX:
1045	CD	BB	10	CALL	SEND_BYTE
1048	CB	7A	BIT	7, D	;Test for ACK bit.
104A	37	SCF
104B	C8	RET	Z	;Return if ACK bit = L with
;carry set.
STOP_BUS:
104C	CD	32	10	CALL	I2C_STOP	;When ACK error – stop bus.
104F	37	SCF
1050	3F	CCF
1051	C9	RET

I2C_RX:
1052	06	08	LD	B, 08	;8 bits to be clocked in.
NEXT1:
1054	DB	0C	IN	A, (PORT_B_DATA)	;Read SDA line on bit 1.
1056	37	SCF
1057	CB	7F	BIT	7, A	;Sample the data bit.
1059	20	01	JR	NZ, H_FOUND
L_FOUND:
105B	3F	CCF
H_FOUND:
105C	CB	11	RL	C	;Shift MSB right.
105E	CD	68	10	CALL	SCL_CYCLE
1061	10	F1	DJ	NZ, NEXT1	;Process next bit.
1063	CD	68	10	CALL	SCL_CYCLE	;Send 'NACK to device.
1066	79	LD	A, C	;Byte from device ready in C.
1067	C9	RET

;Each bit on the SDA line is indicated with a L-H-L sequence on the SCL line. After SCL going High the SDA line is sampled.
SCL_CYCLE:
1068	CD	AB	10	CALL	SCL_OUT	;SCL = L.
106B	CD	66	11	CALL	DELAY
106E	CD	9B	10	CALL	SCL_IN	SCL = H.
1071	CD	66	11	CALL	DELAY
1074	DB	0C	IN	A, (PORT_B_DATA)	;Sample the SDA line.
1076	57	LD	D, A
1077	CD	AB	10	CALL	SCL_OUT
107A	C9

SDA_IN:	;Set SDA high.
107B	3A	00	1B	LD	A, (PORT_B_MODE)
107E	00	NOP
107F	00	NOP
1080	3A	01	1B	LD	A, (PIO_B_IO_CONF)	;Change SDA to input.
1083	CB	FF	SET	7, A
1085	D3	0C	OUT	(PORT_B_CNTRL), A
1087	32	01	1B	LD	(PIO_B_IO_CONF), A
108A	C9	RET

SDA_OUT:	;Set SDA low.
108B	3A	00	1B	LD	A, (PORT_B_MODE)
108E	00	NOP
108F	00	NOP
1090	3A	01	1B	LD	A, (PIO_B_IO_CONF)	;Change SDA to output.
1093	CB	BF	RES	7, A
1095	D3	0C	OUT	(PORT_B_CNTRL), A
1097	32	01	1B	LD	(PIO_B_IO_CONF), A
109A	C9	RET

SCL_IN:	;Set SCL high.
109B	3A	00	1B	LD	A, (PORT_B_MODE)
109E	00	NOP
109F	00	NOP
10A0	3A	01	1B	LD	A, (PIO_B_IO_CONF)	;Change SCL to input.
10A3	CB	C7	SET	0, A
10A5	D3	0C	OUT	((PORT_B_CNTRL), A
10A7	32	01	1B	LD	(PIO_B_IO_CONF), A
10AA	C9	RET

SCL_OUT:	;Set SCL low.
10AB	3A	00	1B	LD	A, (PORT_B_MODE)
10AE	00	NOP
10AF	00	NOP
10B0	3A	01	1B	LD	A, (PIO_B_IO_CONF)	;Change SCL to output.
10B3	CB	87	RES	0, A
10B5	D3	0C	OUT	((PORT_B_CNTRL), A
10B7	32	01	1B	LD	(PIO_B_IO_CONF), A
10BA	C9	RET

SEND_BYTE:	;This routine called by I2C_TX:
10BB	06	08	LD	B, 08	;8 bits to be clocked out.
10BD	4F	LD	C, A	;C reg holds the data byte.
NEXT2:
10BE	CB	79	BIT	7, C	;Sample the MSB of data byte.
10C0	20	05	JR	NZ, H_FOUND2
L_FOUND2:
10C2	CD	8B	10	CALL	SDA_OUT	;Pull SDA low.
10C5	18	03	JR	RLC
H_FOUND:
10C7	CD	7B	10	CALL	SDA_IN	;Release SDA to let it go high.
10CA	CD	66	11	CALL	DELAY
RLC:
10CD	CB	01	RLC	C	;Shift MSB right.
10CF	CD	68	10	CALL	SCL_CYCLE	;Cycle SCL - LHL
10D2	10	EA	DJ	NZ, NEXT2	;Process next bit.
10D4	CD	7B	10	CALL	SDA_IN	;Release SDA to let it go high.
10D7	CD	66	11	CALL	DELAY
10DA	CD	68	10	CALL	SCL_CYCLE	;Cycle SCL - LHL
10DD	C9	RET

I2C_WR:
10DE	CD	25	10	CALL	I2C_START
10E1	3A	02	1B	LD	A, (EEPROM_ADDR)	;Get EEPROM device address.
10E4	CB	87	RES	0, A	:Indicate a write.
10E6	CD	45	10	CALL	I2C_TX	;Send EEPROM device address.
10E9	3E	01	LD	A, 01	;Indicate ACK error - 01.
10BB	32	03	1B	LD	(ERROR_CODE), A
10EE	D0	RET	NC
10EF	7C	LD	A, H
10F0	CD	45	10	CALL	I2C_TX	;Send address high byte.
10F3	3E	02	LD	A, 02	;Indicate ACK error - 02.
10F5	32	03	1B	LD	(ERROR_CODE), A
10F8	D0	RET	NC
10F9	7D	LD	A, L
10FA	CD	45	10	CALL	I2C_TX	;Send address low byte.
10FD	3E	03	LD	A, 03	;Indicate	ACK error - 03.
10FF	32	03	1B	LD	(ERROR_CODE), A
1102	D0	RET	NC
1103	7B	LD	A, E
1104	CD	45	10	CALL	I2C_TX	;Send data byte.
1107	3E	04	LD	A, 04	;Indicate ACK error - 04.
1109	32	03	1B	LD	(ERROR_CODE), A
110C	D0	RET	NC
110D	CD	32	10	CALL	I2C_STOP
1110	C9	RET

I2C_RD:
1111	CD	25	10	CALL	I2C_START
1114	3A	02	1B	LD	(EEPROM_ADDR), A	;Get EEPROM device address.
1117	CB	87	RES	0, A	;Indicate a write.
1119	CD	45	10	CALL	I2C_TX	;Send EEPROM device address.
111C	3E	11	LD	A, 11	;Indicate ACK error - 11.
111E	32	03	1B	LD	(ERROR_CODE), A
1121	D0	RET	NC,
1122	7C	LD	A, H
1123	CD	45	10	CALL	I2C_TX	;Send address high byte.
1126	3E	12	LD	A, 12	;Indicate ACK error - 12.
1128	32	03	1B	LD	(ERROR_CODE), A
112B	D0	RET	NC
112C	7D	LD	A, L
112D	CD	45	10	CALL	I2C_TX	;Send address low byte.
1130	3E	13	LD	A, 13	;Indicate ACK error - 13.
1132	32	03	1B	LD	(ERROR_CODE), A
1135	D0	RET	NC
1136	CD	9B	10	CALL	SCL_IN
1139	CD	66	11	CALL	DELAY
113C	CD	25	10	CALL	I2C_START
113F	3A	02	1B	LD	A, (EEPROM_ADDR)
1142	CB	C7	SET	0, A	;Indicate a read.
1144	CD	45	10	CALL	I2C_TX	;Send EEPROM device address.
1147	3E	14	LD	A, 14	;Indicate ACK error - 14.
1149	32	03	1B	LD	(ERROR_CODE), A
114C	D0	RET	NC
114D	CD	52	10	CALL	I2C_RX	;Receive data byte.
1150	5F	LD	E, A
1151	CD	32	10	CALL	I2C_STOP
1154	C9	RET

ACK_POLLING:	;Wait for acknowledge.
1155	CD	25	10	CALL	I2C_START
1158	3A	02	1B	LD	A, (EEPROM_ADDR)	;Address of EEPROM.
115B	CB	87	RES	0, A	;Indicate a write.
115D	CD	45	10	CALL	I2C_TX	Send EEPROM device address.
1160	30	F3	JR	NC, ACK_POLLING	;Acknowledge sent?
1162	CD	32	10	CALL	I2C_STOP
1165	C9	RET

DELAY:
1166	C9	RET

;Addresses 1167 to 116E left as unused.

I2C_BLOCK_WR:
116F	F5	PUSH	AF
1170	C5	PUSH	BC
1171	D5	PUSH	DE
1172	CD	00	10	CALL	PIO_INIT
1175	D1	POP	DE
1176	C1	POP	BC
1177	F1	POP	AF
1178	3E	AE	LD	A, AE	;EEPROM device address.
ALT_BLOCK_WR:
117A	32	02	1B	LD	(EEPROM_ADDR), A	;Save EEPROM device address.
117D	EB	EX	DE, HL
117E	ED	52	SBC	HL, DE	;Determine block length.
1180	4D	LD	C, L
1181	44	LD	B, H	;Save to byte counter.
1182	EB	EX	DE, HL
1183	03	INC	B
1184	38	26	JR	C, ADDR_ERROR	;End address lower than start	;address.

NEXT3:
1186	5E	LD	E, (HL)
1187	F5	PUSH	AF
1188	C5	PUSH	BC
1189	CD	DE	10	CALL	I2C_WR
118C	30	26	JR	NC, SAVE_ADDR	;Was there an ACK error.
118E	CD	55	11	CALL	ACK_POLLING	;Wait for 'ACK' from EEPROM.

1191	CD	11	11	CALL	I2C_RD	;Read data byte back.
1194	30	1E	JR	NC, SAVE_ADDR	;Was there a ACK error?
1196	7E	LD	A, (HL)

1197	BB	CP	E	;Compare the byte read back with	;the byte in computers memory.

1198	28	27	JR	Z, GOOD	;Is the byte the same?
119A	C1	POP	BC
119B	F1	POP	AF
119C	3E	FF	LD	A, FF
119E	32	03	1B	LD	(ERROR_CODE), A	;Indicate byte read back not the	;same error – FF.

11A1	7C	LD	A, H	;Save address high byte.
11A2	32	04	1B	LD	(HI_ADDR), A	;Address where error occurred.
11A5	7D	LD	A, L
11A6	32	05	1B	LD	(LO_ADDR), A	;Save address low byte.
11A9	C3	53	03	JP	ERROR_MSG
ADDR_ERROR:
11AC	3E	80	LD	A, 80

11AE	32	03	1B	LD	(ERROR_CODE), A	;Indicate end address lower than	;start address error - 80.
11B1	C3	53	03	JP	ERROR_MSG
SAVE_ADDR:	;Save memory address where
11B4	C1	POP	BC	;error occurred.
11B5	F1	POP	AF
11B6	7C	LD	A, H	;Save address high byte.
11B7	32	04	1B	LD	(HI_ADDR), A
11BA	7D	LD	A, L
11BB	32	05	1B	LD	(LO_ADDR), A	;Save address low byte.
11BE	C3	53	03	JP	ERROR_MSG
GOOD:
11C1	C1	POP	BC
11C2	F1	POP	AF
11C3	23	INC	HL
11C4	0B	DEC	BC
11C5	78	LD	A, B
11C6	B1	OR	C
11C7	20	BD	JR	NZ, NEXT3	;Get the next byte.
NO_ERROR:
11C9	3E	00	LD	A, 00
11CB	32	03	1B	LD	(ERROR_CODE), A	;Indicate NO error - 00.
11CE	C9	RET

I2C_BLOCK_RD:
11CF	F5	PUSH	AF
11D0	C5	PUSH	BC
11D1	D5	PUSH	DE
11D2	CD	00	10	CALL	PIO_INIT
11D5	D1	POP	DE
11D6	C1	POP	BC
11D7	F1	POP	AF

11D8	3E	A0	LD	A, AF	;EEPROM Device address.

ALT_BLOCK_RD:
11DA	32	02	1B	LD	(EEPROM_ADDR), A	;Save EEPROM device address.
11DD	EB	EX	DE, HL
11DE	ED	52	SBC	HL, DE	;Determine block length.

11E0	4D	LD	C, L
11E1	44	LD	B, H	;Save to byte counter.
11E2	EB	EX	DE, HL
11E3	03	INC	BC
11E4	38	C6	JR	C, ADDR_ERROR	;End address lower than start	;address.
NEXT4:
11E6	F5	PUSH	AF
11E7	C5	PUSH	BC
11E8	CD	11	11	CALL	I2C_RD	;Read a byte.
11EB	30	C7	JR	NC, SAVE_ADDR	;Was there a ACK error?
11ED	73	LD	(HL), E
11EE	C1	POP	BC
11EF	F1	POP	AF
11F0	23	INC	HL
11F1	OB	DEC	BC
11F2	78	LD	A, B
11F3	B1	OR	C
11F4	20	F0	JR	NZ, NEXT4	;Get the next byte.
11F6	18	D1	JR	NO_ERROR

I2C_RX2:	;Receive a byte of data from a device.
11F8	06	08	LD	B, 08	;8 bits to be clocked in.
NEXT5:
11FA	DB	0C	IN	A, (PORT_B_DATA)	;Read SDA line on bit 1.
11FC	37	SCF
11FD	CB	7F	BIT	7, A	;Test bit 7 for 0 or 1.
11FF	20	01	JR	NZ, H_FOUND3
L_FOUND3:
1201	3F	CCF
H_FOUND3:
1202	CB	11	RL	C	;Shift MSB right.
1204	CD	68	10	CALL	SCL_CYCLE	;L-H-L
1207	10	F1	DJ	NZ, NEXT5	;Process next bit.
1209	79	LD	A, C	;Byte from device ready in A.
120A	C9	RET

SEND_ACK:
120B	CD	8B	10	CALL	SDA_OUT	;SDA = L
120E	CD	68	10	CALL	SCL_CYCLE	;L-H-L
1211	CD	7B	10	CALL	SDA_IN	;SDA = H
1214	C9	RET

SEND_NACK:
1215	CD	7B	10	CALL	SDA_IN	;SDA = H
1218	CD	68	10	CALL	SCL_CYCLE	;L-H-L
121B	C9	RET

RESTART:
121C	CD	9B	10	CALL	SCL_IN	;SCL = H
121F	CD	66	11	CALL	DELAY
1222	CD	25	10	CALL	I2C_START
1225	C9	RET

RTC_BLOCK_WR:	;Load 'HL' with start address of config table before calling this routine.
1226	CD	25	10	CALL	I2C_START
1229	3E	D0	LD	A, D0	;Address of the DS1307 RTC.
122B	CB	87	RES	0, A	;Indicate a write.
122D	CD	45	10	CALL	I2C_TX	;Send address byte.
1230	D2	53	03	JP	NC, ERROR_MSG
1233	3E	00	LD	A, 00	;RTC register 00.

1235	CD	45	10	CALL	I2C_TX	;Send byte for register 00.
1238	D2	53	03	JP	NC, ERROR_MSG
123B	06	08	LD	B, 08	;8 bytes to be sent next.
NEXT6:
123D	C5	PUSH	BC
123E	7E	LD A, (HL)	;Get data byte from config table.
123F	CD	45	10	CALL	I2C_TX	;Send data byte.
1242	D2	53	03	JP	NC, ERROR_MSG
1245	C1	POP	BC
1246	23	INC	HL	;Point to next byte in the table.
1247	10	F4	DJ	NZ, NEXT6	;Repeat.
1249	CD	32	10	CALL	I2C_STOP
124C	C9	RET

RTC_BLOCK_RD:	;Load 'HL' with start address of config table before calling this routine.
124D	CD	25	10	CALL I2C_START
1250	3E	D0	LD	A, 00	;Address of the DS1307 RTC.
1252	CB	87	RES	0, A	;Indicate a write.
1254	CD	45	10	CALL	I2C_TX	;Send address byte.
1257	D2	53	03	JP	NC, ERROR_MSG
125A	3E	00	LD	A, 00	;RTC register 00.
125C	CD	45	10	CALL	I2C_TX	;Send byte for register 00.
125F	D2	53	03	JP	NZ, ERROR_MSG

1262	CD	1C	12	CALL	RESTART
1265	3E	D0	LD	A, D0	;Address of the RTC.
1267	CB	C7	SET	0, A	;Indicate a read.
1269	CD	45	10	CALL	I2C_TX	;Send Address byte.
126C	D2	53	03	JP	NC, ERROR_MSG
126F	06	07	LD	B, 07	;7 bytes to receive.
NEXT7:
1271	C5	PUSH	BC
1272	CD	F8	11	CALL	I2C_RX2	;Read in data byte.
1275	77	LD	A, (HL)	;Save byte to config table.
1276	CD	0B	12	CALL	SEND_ACK	;Request to receive another byte.
1279	C1	POP	BC
127A	23	INC	HL	;Point to next table location.
127B	10	F4	DJ	NZ, NEXT7
127D	CD	F8	11	CALL	I2C_RX2	;Read in last data byte.
1280	77	LD	A, (HL)	;Save byte to config table.
1281	CD	15	12	CALL	SEND_NACK	;Request to stop receiving bytes.
1284	CD	32	10	CALL	I2C_STOP
1287	C9	RET

;END